Supplementary code file:

The Labchart program is used for automating the transformed-rule up and down testing procedure. The user program presents stimuli of specified amplitudes and collects and checks correctness of responses. Labchart has a built-in support for command scripts and a stimulator feature that allows the generation of a wide variety of stimulus waveforms. Stimulus waveforms can be outputted using the PowerLab analog outputs. The analog outputs provide a computer-controlled variable voltage output that can be used to control peripheral devices. Please install the Labchart Event Manager Add-On. The Event Manager Add-On for LabChart monitors incoming signals and detects user-defined events. Here, the incoming signals from the response box button 1 and 2 are detected.

Macro script for the transformed-rule up and down procedure:

1. Script variables:

| Variables for the Labchart program |
| --- |
| Variables | Comments |
| startingamplitude=23 | Starting amplitude set at intensity level 23 |
| testingamplitude=0 | Amplitude step that will be applied in the next stimulation |
| rndmseq | Random sequence of numbers |
| response=0 | Response of subject |
| correct_count=0 | Count of correct responses |
| incorrect_count=0 | Count of incorrect responses |
| cycle=1 | Number of testing cycles |
| writeresponse | Writes if response of subject is correct or incorrect in datapad for each trial |
| amplitudechange=0 | States if criteria for amplitude change were met and indicates direction of amplitude change (up or down) |
| changestatus=0 | States if amplitudes are currently changing towards up or down |
| firstrev=0 | Indicates if the first amplitude change is in “up” or “down” direction |
| changecount=1 | Counts how many times amplitude intensity was changed (starts on 1) |
| prevstatus=0 | Equals variable “changestatus” from the previous cycle |
| reversalcount=0 | Counts the number of reversals of amplitude change directions (from up to down or vice versa).Note that this variable will have the value “1” after the first amplitude change. After first reversal value will be “2” |
| amplitudevoltage | Voltage value to set stimulus intensity |

2. Macro script:

startingamplitude=23

testingamplitude=0

rndmseq

response=0

correct_count=0

incorrect_count=0

cycle=1

writeresponse

amplitudechange=0

changestatus=0

firstrev=0

changecount=1

prevstatus=0

reversalcount=0

Amplitudevoltage

Call Doc.StartSampling

Starts sampling of the selected device.

Call Doc.GetDataPadValue (startingamplitude)

testingamplitude = Doc.GetDataPadValue (startingamplitude)

Sets the value of testingamplitude to the corresponding amplitude intensity listed in the Data Pad column 2. In this case this is the startingamplitude level of 23.

SetStimulatorValue

Changes the value and units of a parameter being used by the outputs.

Output channel = 1

amplitude value = testingamplitude

Sets the amplitude intensity to use for output 1.

Call Doc.SetStimulatorOn

Change the On/Off state of the output.

if rndmseq = interval1

then Call Doc.SetStimulatorWaveform (output 1, "User waveform – stim1")

if rndmseq = interval2

then Call Doc.SetStimulatorWaveform (output 1, "User waveform – stim2")

Chooses the waveform to use for output 1 (piezoelectric actuator). Rndmseq is an arbitrary sequence of numbers (interval1 & 	interval2)

Call Doc.SetStimulatorWaveform (output 2, "User waveform – clue")

Chooses the waveform to use for output 2 (Monitor)

Call Doc.StimulateNow ()

Stimulation occurs immediately

Call WaitFor (hours=0, minutes=0, seconds=7.75)

Waits for a set length of time, which is the duration length of one trial, 	before the macro continues.

Call Script.RegisterScriptEvent (0, "Comment Added", "OnCommentAdded")

Register events occurring in input channel 1 recording response box.

Button 1 of response box triggers a > 1 V input

Button 2 of response box triggers a < -1 V input

Call Doc.Find (channel 1, “event”)

Selects the registered event value (signal < -1 V or > 1 V)

Call Doc.ReplaceDataPadRowWithCurrentSelection()

Replaces data 	value in 2 specified row in datapad

Call Doc.GetDataPadValue()

Returns the value at the specified cell in the Data pad

if Call Doc.GetDataPadValue() > 1 then response = interval1

if Call Doc.GetDataPadValue() < -1 then response = interval2

Determines if subject chose first or second interval as response

if (response=rndmseq) then

correct_count=correct_count+1

cycle=+1

writeresponse=”correct”

end if

Registers if response was correct, then adds to count of correct responses and to overall cycle count

if not(response= rndmseq) then

incorrect_count=incorrect_count+1

cycle=cycle+1

writeresponse=”incorrect”

end if

Registers if response was correct, then adds to count of correct responses and to overall cycle count.

Call Doc.SetDataPadValue(sheet number, row = incorrect_count+correct_count, column= changecount+1, value= writeresponse)

if (incorrect_count>2 or (incorrect_count>1 and correct_count<5)) then 		amplitudechange=1

Registers if criteria for amplitude increase are met (up rule)

if (correct_count>6 or (correct_count>5 and incorrect_count<2)) then 	amplitudechange=-1

Registers if criteria for amplitude decrease are met (down rule)

if (amplitudechange = 1 or amplitudechange =-1) then

correct_count = 0

incorrect_count = 0

end if

Resets incorrect and correct response counts once amplitude level changes.

if (amplitudechange=1 or amplitudechange=-1)

then changestatus = amplitudechange

Updates if direction of amplitude change occurs

if (changecount=1 and amplitudechange=1) then firstrev=1

if (changecount=1 and amplitudechange=-1) then firstrev=-1

Detects the direction (up or down) of first amplitude change.

if (amplitudechange=1 or amplitudechange=-1)

then changecount = changecount+1

Detects change in amplitude and adds 1 change to the count

if (changestatus<prevstatus or changestatus>prevstatus)

then reversalcount=reversalcount+1

Detects reversal in direction of amplitude changes and adds 1 to the count

if ((changestatus<prevstatus or changestatus>prevstatus) and reversalcount>1)

then Call Doc.SetDataPadValue(sheet number, row = reversalcount, column, value = startingamplitude)

Sets the value of the amplitude at reversal at a specified cell in Datapad

prevstatus = changestatus

Sets prevstatus for use in next cycle

if reversalcount < 3

then amplitudechange = amplitudechange*4

Changes the number of steps in amplitude change from 1 to 4 if an amplitude change is triggered, and if reversal 3 has not been reached.

if ((reversalcount = 4 and firstrev=-1) or (reversalcount = 3 and firstrev = 1)) then 	amplitudechange = 	amplitudechange*2

Changes the number of steps in amplitude change from 1 to 2 if an amplitude change is triggered, and if the amplitudes are currently changing in the “up” direction for the second time

startingamplitude = startingamplitude+amplitudechange

Changes amplitude intensity level (in steps) that will be applied during next stimulation.

if ((amplitudechange>=1 or amplitudechange<=-1) and reversalcount<9)

then Call Doc.SetDataPadValue(sheet number, row, column= changecount+1, value= testingamplitude)

Gets the voltage value corresponding to the stimulus intensity level (in steps) from the datapad.

Call Doc.GetDataPadValue (1, startingamplitude, 2)

testingamplitude = Doc.GetDataPadValue (1, testingamplitude, 2)

amplitudechange =0

Resets amplitude change for next cycle

if reversals = 9 then Call Services.StopMacroExecution

Ends macro after 8 reversals

Call Doc.SetDataPadValue(sheet, row, column, changecount)

Call Doc.SetDataPadValue(sheet, row, column, reversalcount)

Call Doc.SetDataPadValue(sheet, row, column, startingamplitude)

Call Doc.SetDataPadValue(sheet, row, column, testingamplitude)

Sets the values at a specified cell in Datapad

Call Doc.GetDataPadValue (1, cycle+1, 1)

rndmseq=Doc.GetDataPadValue (1, cycle+1, 1)

With this command a new cycle (trial) is initiated.

SetStimulatorValue

Changes the value and units of a parameter being used by an outputs.

Output channel = 1

amplitude value = testingamplitude

Chooses the amplitude intensity to use for output 1

Call Doc.SetStimulatorOn

Change the On/Off state of the output.

if rndmseq = interval1

then Call Doc.SetStimulatorWaveform (output 1, "User waveform – stim1")

if rndmseq = interval2

then Call Doc.SetStimulatorWaveform (output 1, "User waveform – stim2")

Chooses the waveform to use for output 1 (piezoelectric actuator). Rndmseq is an arbitrary sequence of numbers (interval1 & 	interval2)

Call Doc.SetStimulatorWaveform (output 2, "User waveform – clue")

Chooses the waveform to use for output 2 (Monitor)

Call Doc.StimulateNow ()

Stimulation occurs immediately

End Sub